## Slide 1: CO2015 Diode & Its Applications

## Slide 2: Diode and Its Applications
Introduction to semiconductor
Diode
Applications

## Slide 3: Semiconductor
Semiconductors are a special class of elements having a conductivity between that of a good conductor and that of an insulator.
Two classes: single-crystal and compound
The three semiconductors used most frequently in the construction of electronic devices are Ge, Si, and GaAs.

## Slide 4: Germanium (Ge)
The discovery of the diode in 1939 and the transistor in 1947 germanium was used almost exclusively
Advantages
  Easy to find
  Fairly large quantities
  Easy to refine to obtain very high levels of purity
Disadvantage
  Sensitivity to changes in temperature

## Slide 5: Silicon (Si)
1954 the first silicon transistor was introduced
Advantages
  Less temperature sensitive
  The most abundant materials on earth
  High levels of purity
Disadvantage
  Sensitive to issues of speed.

## Slide 6: Gallium Arsenide (GaAs)
The first GaAs transistor in the early 1970s.
New transistor had speeds of operation up to five times that of Si.
GaAs was more difficult to manufacture at high levels of purity, was more expensive.
Today, it is often used as the base material for new high-speed, very large scale integrated (VLSI) circuit designs.

## Slide 7: Diode
The diode is the simples and most fundamental non-linear circuit element
Like a resistor, it has two terminals
Unlike a resistor, it has a non-linear current-voltage characteristics.
Its use in rectifiers is
the most common application

## Slide 8: Diodes
Diode is composed of P and N semiconductors
Diode is ON when VAC ≥ 0.7V
Diode if OFF when 0 ≥ VAC ≥ - 1000V
Out of this range, diode is broken

## Slide 9: Diode Application - Reverse Current Protection
Mandatory design for any system
Drawback: around 0.7V loss because of the forward voltage drop.

## Slide 10: Diode Application - AC to DC Converter

## Slide 11: Diode Application - Rectifier
Convert Alternating Current (AC) to Direct Current (DC)
  Half wave rectifier
  Full wave rectifier

## Slide 12: Logic Gates
OR
AND

## Slide 13: Diode Checking using OPAM
Black – Anode (Red – Cathode): Cursor moves ON
Reverse connection: Cursor stops

## Slide 14: Diode
Diode is an electric device which allows current to flow only in one direction.
The voltage applied to the semi conductor diode is referred to as bias voltage
There are two types of bias voltage
  Forward biased
  Reversed biased

## Slide 15: PN Junction and Diode (Video)

## Slide 16: PN Junction and Diode
One end of a silicon or germanium crystal can be doped as a p-type material and the other end as an n-type material.
At the p-n junction, the excess conduction-band electrons on the n-type side are attracted to the valence-band holes on the p-type side.
Notes: The electrons in the n-type material migrate across the junction to the p-type material (electron flow).
Electron migration results in a negative charge on the p-type side of the junction and a positive charge on the n-type side of the junction.
The result is the formation of a depletion region around the junction

## Slide 17: Diode – No Bias
No external voltage is applied: VD = 0 V
There is no diode current: ID = 0 A
Only a modest depletion region exists

## Slide 18: Diode – Forward Bias
External voltage is applied across the p-n junction in the same polarity as the p- and n-type materials.
The forward voltage causes the depletion region to narrow.
The electrons and holes are pushed toward the p-n junction.
The electrons and holes have sufficient energy to cross the p-n junction

## Slide 19: Diode – Reverse Bias
External voltage is applied across the p-n junction in the opposite polarity of the p- and n-type materials.
The reverse voltage causes the depletion region to widen.
The electrons in the n-type material are attracted toward the positive terminal of the voltage source.
The holes in the p-type material are attracted toward the negative terminal of the voltage source.

## Slide 20: Diode Equivalent Circuit

## Slide 21: Load-Line Analysis

## Slide 22: Diode Symbol and Packaging
The anode is abbreviated A
The cathode is abbreviated K

## Slide 23: Diode Testing
Diodes are commonly tested using one of these types of equipment:
  Diode checker
  Ohmmeter
  Curve tracer

## Slide 24: Diode Checker
Many digital multimeters have a diode checking function. The diode should be tested out of circuit.
A normal diode exhibits its forward voltage:
  Gallium arsenide  1.2 V
  Silicon diode  0.7 V
  Germanium diode  0.3 V

## Slide 25: Ohmmeter
An ohmmeter set on a low Ohms scale can be used to test a diode. The diode should be tested out of circuit.

## Slide 26: Curve Tracer
A curve tracer displays the characteristic curve of a diode in the test circuit. This curve can be compared to the specifications of the diode from a data sheet.

## Slide 27: Other Types of Diodes
There are several types of diodes besides the standard p-n junction diode. Three of the more common are:
  Zener diodes
  Light-emitting diodes
  Diode arrays

## Slide 28: Zener Diode
A Zener diode is one that is designed to safely operate in its zener region; i.e., biased at the Zener voltage (VZ).
Common zener diode voltage ratings are between 1.8 V and 200 V

## Slide 29: Light-Emitting Diode (LED)
An LED emits light when it is forward biased, which can be in the infrared or visible spectrum.
The forward bias voltage is usually in the range of 2 V to 3 V.

## Slide 30: Diode Arrays
Multiple diodes can be packaged together in an integrated circuit (IC).
A variety of diode configurations are available.
Common Anode
Common Cathode

## Slide 31: Half-Wave Rectification
Convert AC to DC using one Diode
AC: Alternating Current DC: Direct Current
Rectifier

## Slide 32: Half-Wave Rectification (cont.)

## Slide 33: Full-Wave Rectification
Convert AC to DC using two or four diodes
Full-Wave
Rectifier

## Slide 34: Complete AC/DC Power Circuit

## Slide 35: DC Adapter Circuits (Zenner Diode)

## Slide 36: Bridge Rectifier

## Slide 37: Ripple in Rectification

## Slide 38: Ideal Diode Model
Works as a switch
  Forward bias (switch is close)
  Reverse bias (switch is open)
Threshold battery voltage and internal resistance are ignored.
Forward bias
Reverse bias

## Slide 39: Practical Diode Model
Constants
  Silicon Diode: VF = 0.7V (VF = VBIAS if VBIAS < 0.7V)
  Germanium Diode: VF = 0.3V (VF = VBIAS if VBIAS < 0.3V)
Forward bias
Reverse bias

## Slide 40: Complete Diode Model
Forward bias
Reverse bias

## Slide 41: Exercise 1
Determine VD, ID and VR based on the characteristic of the diode given in the following figure.

## Slide 42: Solution 1

## Slide 43: Exercise 2
Determine
  I1, ID1, ID2

## Slide 44: Exercise 3
Given circuit
  Forward bias voltage VF = 0.7V
  Internal resistance
Determine VF, IF and VRLIMIT for three diode models
  Ideal diode model
  Practical diode model
  Complete diode model

## Slide 45: Solution Ex.3
Ideal diode model
Practical diode model
Complete diode model

## Slide 46: Exercise 4
Given circuit
  Reverse current
Determine VF, IF and VR for three diode model từng
  Ideal diode model
  Practical diode model
  Complete diode model

## Slide 47: Exercise 5
Analyze and validate the value of the voltmeter in case of using ideal diode model ?